## Slide 1
CSOPESY · MO3 · TECHNICAL REPORT
_____ _____ _____ ______ _____ _____ __ __
/ __ \ / ___| | _ | | ___ \ | ___| / ___| \ \ / /
| / \/ \ `--. | | | | | |_/ / | |__ \ `--. \ V /
| | `--. \ | | | | | __/ | __| `--. \ \ /
| \__/\ /\__/ / \ \_/ / | | | |___ /\__/ / | |
\____/ \____/ \___/ \_| \____/ \____/ \_/
Marquee Console
Console UI · Command interpreter · Display · Marquee animation · Refresh vs. polling rate
GROUP DEVELOPER
Obcena, Hans Gabriel
Suerte, Lorenzo Enrique
Cordero, Ramuel Sean
Eleydo, Renzel Vince
Version date: 2026-09-21 · github.com/Enzo-user/CSOPESY_MO3
Notes: Marquee Console, CSOPESY MO3 technical report. The banner is drawn with the same ascii_big.txt font and the same crop-plus-kerning rule the program uses. The deck follows the quiz's five topics: console UI, command interpreter, display, marquee animation logic, and the refresh-rate versus polling-rate balance.

## Slide 2
00 / OVERVIEW
System at a glance
src/main.cpp → int main() { MarqueeConsole console; console.run(); }
MarqueeConsole
welcome header · Command> loop · command interpreter · keyboard polling
Config
config.txt settings read at startup
AsciiFont
ascii_big.txt glyphs → 8 text rows
Metrics
timings behind the stats command
Console
ANSI, layout, the one output mutex
Marquee
text, speed and the animation thread
SHARED HELPERS
DataFile
finds config.txt and ascii_big.txt (working dir, then exe dir)
Text
trim() and the millisecond parser used by both inputs
Only Console, DataFile and MarqueeConsole touch the Windows API; the rest is portable C++.
9
.cpp source files
1,031
lines of C++ in src/
2
threads: console + marquee
56 / 56
smoke-test checks pass
Notes: One class per job. main() creates a single MarqueeConsole, which owns everything else in destruction order: the marquee thread is joined before the Console restores the window. Two threads run: the console thread (input and commands) and the marquee thread (animation). The Windows-specific code is isolated in three units, so Config, AsciiFont, Metrics and Text are covered by a portable smoke test (56 checks).

## Slide 3
01 / CONSOLE UI IMPLEMENTATION
Console UI: a shell-style transcript
marquee.exe - 120 x 30
Welcome to CSOPESY!
Group developer:
Obcena, Hans Gabriel
Suerte, Lorenzo Enrique
Cordero, Ramuel Sean
Eleydo, Renzel Vince
Version date: 2026-09-21
Config: text "Hello, World!", refresh 100 ms, polling 10 ms
Command> help
help - displays the commands and its description
start_marquee - starts the marquee "animation"
stop_marquee - stops the marquee "animation"
set_text - accepts a text input and displays it as a marquee
set_speed - sets the marquee animation refresh in milliseconds
exit - terminates the console
Command> set_text Operating Systems are fun!
Text saved for marquee: Operating Systems are fun!
Command> _
1
Welcome header
header_text() prints the sample's layout: banner, "Group developer:" with the four members, and "Version date:". A Config: line then shows the values loaded from config.txt.
2
Prompt and line editor
"Command> " is printed and each key is read with _kbhit()/_getch(). The line is redrawn in place (\r, ESC[2K, prompt + text). Backspace edits, arrow and F-keys are ignored, and long lines show only their tail.
3
Scrolls like a real shell
Output scrolls upward inside an ANSI scroll region (ESC[1;21r), so commands and replies behave like PowerShell or cmd while the marquee keeps the bottom rows.
4
Clean exit
exit, Ctrl+C or closing the window clears the marquee rows and resets the region (ESC[r), leaving a normal console.
Notes: The console is a transcript, not a redrawn menu: the header prints once, then every prompt, command and reply scrolls upward like a normal shell. Input is read one key at a time instead of with std::getline, because a blocking read would freeze the console thread; the prompt line is repainted after every key. The screen on the left is the program's actual output, read back from the console buffer.

## Slide 4
02 / COMMAND INTERPRETER IMPLEMENTATION
Command interpreter: from keystroke to command
Poll
_kbhit() every
polling-rate ms
Read
_getch() builds the
line until Enter
Trim
text::trim() strips
spaces, tabs, \r
Split
first whitespace →
command | argument
Dispatch
command == "help"
… std::string compare
Command | What the interpreter does | Console reply
help | Prints the six commands and their descriptions | help - displays the commands and its description …
start_marquee | marquee_.start(): running = true, draw a frame at once | Marquee animation started.
stop_marquee | marquee_.stop(): running = false, clear rows 23–30 | Marquee animation stopped.
set_text <text> | Keeps the rest of the line (inner spaces kept); empty → usage error | Text saved for marquee: <text>
set_speed <ms> | parse_milliseconds(): digits only, 1 to 999,999,999 | Marquee speed set to <ms> milliseconds.
exit | Returns false: loop ends, thread joined, screen restored | Terminating console...
anything else | No match (case-sensitive, like the sample) | Unrecognized command: <word>. Type 'help' …
Hidden diagnostics for this report: stats and set_poll <ms> (not listed by help). Invalid set_speed values (abc, 0, -5, 10x, empty) print a usage error and keep the old speed.
Notes: Command recognition happens in two places. read_command_line() turns keystrokes into a line; execute() trims it, splits at the first whitespace into command and argument, and compares the command with std::string equality. set_text keeps everything after the command, so text with spaces survives. set_speed accepts only whole positive numbers of milliseconds. Every row in the table was checked against the running program.

## Slide 5
03 / DISPLAY IMPLEMENTATION
Display: two screen regions, one lock
actual screen, marquee running (first 100 of 120 columns)
Welcome to CSOPESY!
Group developer:
Obcena, Hans Gabriel
Suerte, Lorenzo Enrique
Cordero, Ramuel Sean
Eleydo, Renzel Vince
Version date: 2026-09-21
Config: text "Hello, World!", refresh 100 ms, polling 10 ms
Command> set_text Operating Systems are fun!
Text saved for marquee: Operating Systems are fun!
Command> start_marquee
Marquee animation started.
Command> set_sp
_ _ _____ _
| | (_) / ___| | |
_ __ __ _ | |_ _ _ __ __ _ \ `--. _ _ ___ | |_ ___ _ __ ___ ___
'__| / _` | | __| | | | '_ \ / _` | `--. \ | | | | / __| | __| / _ \ | '_ ` _ \ / __|
| | (_| | | |_ | | | | | | | (_| | /\__/ / | |_| | \__ \ | |_ | __/ | | | | | | \__ \
_| \__,_| \__| |_| |_| |_| \__, | \____/ \__, | |___/ \__| \___| |_| |_| |_| |___/
__/ | __/ |
|___/ |___/
Rows 1–21: transcript (scroll region ESC[1;21r)
Row 22: blank separator
Rows 23–30: marquee (8-row font)
1
Layout from the window size
At startup Console reads the window height: the transcript gets rows 1 to height − 10, the marquee the last 8 rows.
2
Cursor-safe frames
A frame is ESC[s, then per row: move to row, ESC[2K, 119 characters, then ESC[u. The user's cursor never moves.
3
One lock, one write
Every std::cout write goes through Console's mutex. A frame is built as one string and flushed once (0.16–0.19 ms).
4
No ghost frames
write_if() re-checks running under the lock, so a frame built just before stop_marquee is dropped, not drawn over cleared rows.
Notes: The display is split into two regions of one window. The ANSI scroll region keeps all transcript scrolling above the marquee, and the marquee thread paints its eight rows with absolute cursor moves wrapped in save/restore, so typing continues where the user left it. Both threads write through the same mutex, which prevents interleaved escape sequences, the main cause of garbled output in multi-threaded consoles. The screen shown is the program's real buffer, captured mid-animation.

## Slide 6
04 / MARQUEE ANIMATION LOGIC
Marquee animation: a sliding 8-row window
1
Load the font
ascii_big.txt holds 94 glyphs ('!' to '~'), 8 rows each. Every glyph is cropped to its width plus one column of kerning; a space is 5 columns.
2
Render the text
render(text) stitches the glyphs side by side into 8 strings, one per screen row. Unknown characters become a gap.
3
Slide the window
Screen column i shows pattern[(offset + i) % length], where pattern = row + 3 spaces. offset++ each frame moves the text one column left and wraps it around seamlessly.
one row, window of 22 columns
pattern "HELLO "
offset 0 |HELLO HELLO HELLO |
offset 1 |ELLO HELLO HELLO |
offset 2 |LLO HELLO HELLO |
src/Marquee.cpp (simplified)
// Marquee::run(), the marquee thread
while (alive_) {
auto now = steady_clock::now();
if (running_ &&
(frame_requested_ || now >= next_frame)) {
bool forced = frame_requested_.exchange(false);
draw_frame(font_.render(text()), offset);
++offset; // one column left
auto interval = ms(refresh_ms_.load());
next_frame = forced ? now + interval
: next_frame + interval;
if (next_frame < now)
next_frame = now; // resume, no catch-up
}
sleep_for(ms(TICK_MS)); // TICK_MS = 10
}
Why a deadline instead of sleep(refresh)?
next_frame += interval keeps the average exactly on the set speed (100 ms → 100.10 ms measured). start_marquee and set_speed request a frame at once, so changes show without waiting out the old interval.
Notes: The animation never moves the text itself: it moves a window over a repeating pattern. Each of the eight rendered rows is treated as a ring buffer, and the frame shows the width of the console starting at offset. Incrementing offset scrolls one column to the left and the modulo makes the text wrap around. The thread wakes on a 10 ms tick to react quickly to start, stop and speed changes, but only draws when a frame is due.

## Slide 7
05 / PROCESS REPRESENTATION & SCHEDULING
Two threads, scheduled by the OS
Console thread (main)
loop:
if !_kbhit(): sleep(polling_ms)
else: key = _getch()
edit line, redraw prompt
on Enter: execute(command)
Marquee thread
every TICK_MS (10 ms):
if running and due:
draw frame, offset++
next_frame += refresh_ms
exits when alive_ = false
Shared state | Protected by | Written by → read by
text_ | std::mutex | set_text → marquee thread
running_ | std::atomic<bool> | start / stop_marquee → marquee
refresh_ms_ | std::atomic<int> | set_speed → marquee
frame_requested_ | std::atomic<bool> | start, set_speed → marquee
alive_ | std::atomic<bool> | destructor on exit → marquee
std::cout | Console::mutex_ | both threads
THE REAL SCHEDULER
15.6 ms
Windows timer tick: the shortest real sleep
Both loops only pick sleep lengths; Windows decides when a thread runs again.
Measured: sleep(1 ms) lasted 15.5 ms, and set_speed 1 gave a frame every 15.6 ms.
Longer sleeps round up to the next tick: set_poll 20 → 31.0 ms.
Notes: Process representation: the program is one process with two threads. The console thread owns input and command execution; the marquee thread owns the animation. They communicate only through the fields in the table, each either atomic or guarded by a mutex, and every write to std::cout goes through one lock. Scheduling: neither thread busy-waits. Each sleeps and the Windows scheduler wakes it on its timer tick, about 15.6 ms by default. That tick sets the floor for both the refresh rate and the polling rate, as the next slides show.

## Slide 8
06 / FINDING THE BALANCE
Refresh rate vs. polling rate
Refresh rate
config.txt refresh-rate · set_speed <ms>
How often the marquee thread redraws the 8 rows.
Too fast: frames outpace the console's repaint (tearing, skipped columns).
Too slow: the text crawls and looks choppy.
Polling rate
config.txt polling-rate · set_poll <ms>
How often the console thread checks _kbhit().
Too fast: no gain below the timer tick, only extra wake-ups.
Too slow: typed characters appear late or in bursts.
How we measured
Ran the release build in a 120 × 30 console with the marquee running.
For each value: set it, type about 70 keystrokes over 8 s, then read stats (frame interval, late frames, draw time, polling sleep, key-to-screen).
Changed one knob at a time: polling held at 10 ms for the refresh sweep, refresh held at 100 ms for the polling sweep.
Test hardware | 
CPU | AMD Ryzen 5 5600 (6 cores / 12 threads)
Memory | 32 GB
OS | Windows 11 Pro (build 26200)
Display | Radeon RX 9060 XT, 2560 × 1440 at 120 Hz
Build | C++17, -O2 (Clang / MinGW-w64)
An earlier MSVC Release build on the same CPU (docs/MEASUREMENTS.md) gave the same picture: 100 ms → 99.97 ms, polling floor 15.49 ms.
Notes: The two knobs belong to different threads, so the goal is the smoothest marquee that never makes typing feel late. The stats command reports what actually happened rather than what was requested. Each run changed one value and held the other fixed.

## Slide 9
06 / RESULTS: REFRESH RATE
Below ~16 ms, set_speed stops mattering
Chart: set_speed (ms)
| 1 | 5 | 10 | 16 | 20 | 33 | 50 | 100
Requested (set_speed) | 1 | 5 | 10 | 16 | 20 | 33 | 50 | 100
Measured average interval | 15.62 | 15.61 | 15.61 | 16.02 | 20.02 | 33.03 | 50.04 | 100.1
Measured longest interval | 16.78 | 16.75 | 16.85 | 31.68 | 32.84 | 47.92 | 63.66 | 110.84
set_speed | late / drawn | reading
1 | 542 / 543 | timer floor
5 | 543 / 544 | timer floor
10 | 532 / 544 | timer floor
16 | 13 / 530 | rare 31 ms gap
20 | 119 / 424 | 15.6 / 31.2 ms stutter
33 | 0 / 257 | smooth
50 | 0 / 170 | smooth
100 | 0 / 85 | smooth
250 | 0 / 34 | smooth
1000 | 0 / 13 | smooth
A frame is late when it arrives more than 1.5 × set_speed after the previous one. Drawing a frame took 0.16–0.19 ms at every setting, so the terminal was never the bottleneck.
Notes: Requested versus measured frame interval. From 33 ms up the average matches the setting almost exactly and no frames are late. Below about 16 ms the line goes flat: 1, 5 and 10 ms all produce a frame every 15.6 ms because the thread cannot sleep shorter than one Windows timer tick. Between 16 and 20 ms the average is still right, but individual intervals alternate between one and two ticks (15.6 and 31.2 ms), which shows as uneven motion.

## Slide 10
06 / RESULTS: POLLING RATE
Typing lag grows with the polling interval
Chart: set_poll (ms)
| 1 | 5 | 10 | 15 | 20 | 33 | 50 | 100 | 200
Worst-case typing delay (ms) | 17.02 | 16.91 | 17.03 | 31.37 | 33.3 | 48.22 | 64.01 | 111.94 | 215.23
~100 ms: delay becomes noticeable | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
set_poll | sleep avg | worst | feel*
1 | 15.5 | 17.0 | instant
5 | 15.5 | 16.9 | instant
10 | 15.5 | 17.0 | instant
15 | 16.7 | 31.4 | instant
20 | 31.0 | 33.3 | instant
33 | 46.6 | 48.2 | instant
50 | 62.1 | 64.0 | fine
100 | 108.8 | 111.9 | noticeable
200 | 202.9 | 215.2 | laggy
500 | 511.3 | 515.2 | bursts
Worst = longest polling sleep + longest key-to-screen time (0.15–0.50 ms). *Judged against the ~100 ms point at which input lag becomes perceptible.
Notes: Worst-case typing delay is the longest polling sleep plus the time to echo the key, which is always under half a millisecond, so the delay is almost entirely the polling interval. Values up to 15 ms all measure the same 15.5 ms floor. Above that the delay follows the setting rounded up to whole timer ticks: 20 ms becomes 31 ms, 50 becomes 62 ms, and 100 becomes about 109 ms, where typing starts to feel behind. The 500 ms row (515 ms) is left out of the chart to keep its scale readable.

## Slide 11
06 / RECOMMENDED VALUES & LIMITS
Recommended: refresh 100 ms, polling 10 ms
100 ms
refresh-rate · set_speed
Smooth, readable scroll. Everything from 33 ms up had 0 late frames; typing stayed at ≈17 ms.
10 ms
polling-rate · set_poll
Worst typing delay 17 ms. Anything ≤ 15 ms measures the same, so going lower buys nothing.
Refresh limit
< 16 ms
Capped at the 15.6 ms tick (~64 fps): nearly every frame is late and frames outpace a ~60 Hz console repaint, the zone where tearing and skipped columns appear.
16–20 ms
Intervals alternate between 15.6 and 31.2 ms, so the scroll stutters.
≥ 33 ms
0 late frames: smooth.
Polling limit
≤ 15 ms
All identical (15.5 ms floor); lower values only add wake-ups.
100 ms
Worst delay 112 ms: typed characters start to feel late.
≥ 200 ms
215–515 ms: characters arrive in bursts.
The two rates don't compete: a frame costs 0.18 ms to draw, so typing delay stayed ≈17 ms even at set_speed 1.
Notes: Recommendation for this hardware: refresh 100 ms and polling 10 ms, the shipped defaults. Refresh can go down to about 33 ms if a faster marquee is wanted. Limits: below 16 ms the refresh rate is capped by the timer tick and frames arrive faster than the console repaints, which is where tearing appears; at 16 to 20 ms the scroll stutters. For polling, the delay becomes noticeable at 100 ms and bursty at 200 ms and above. The tearing zone below 16 ms is inferred from the timing data; confirm it by eye on the machine used for the demo.

## Slide 12
BLACK-BOX TEST CASES
A test case only touches config.txt
config.txt (edited for a test case)
marquee_text "CSOPESY MO3"
refresh-rate 250 # edited
polling-rate 20
bogus-key 5
what the program printed on Run
Version date: 2026-09-21
Config: unknown setting 'bogus-key' ignored.
Config: text "CSOPESY MO3", refresh 250 ms, polling 20 ms
Command> start_marquee
Marquee animation started.
Command> stats reset
Statistics reset.
Command> stats
Refresh : set 250 ms | measured avg 249.97, max 252.92, last 252.27 ms
1
Edit config.txt
In the IDE or Notepad++, the only file the quiz allows to change. Keys: marquee-text, refresh-rate, polling-rate ("_" and "-" are interchangeable).
2
Press Run/Debug
The file is read once at startup from the working directory (the Visual Studio project folder) or next to the .exe. No code change is needed.
3
Check the header
The Config: line shows the values in force. An unknown key or unusable value prints a note and keeps the default, so a typo is visible before the test starts.
set_text and set_speed still override the file for the rest of that run.
Notes: The black-box quiz forbids touching the code during a test case; only config.txt may be edited. The program reads marquee text, refresh rate and polling rate from that file at startup and prints the values in force under the header, so the recording itself shows which parameters were used. Both panels are real: the edited file and the output it produced.

## Slide 13
SPECIFICATION CHECKLIST
Every required feature, verified on the running build
Requirement (MO3 specification) | Implementation | Result
Main menu console: Welcome, Group developer, Version date, Command> | header_text(), MarqueeConsole::run() | Pass
Text or ASCII-graphics marquee | AsciiFont + Marquee thread, bottom 8 rows | Pass
Commands change the marquee's behaviour | set_text, set_speed, start / stop_marquee | Pass
help | help_text(): the six commands and descriptions | Pass
start_marquee / stop_marquee | Marquee::start() / stop(), rows cleared on stop | Pass
set_text | Saved under a mutex; shown on the next frame | Pass
set_speed | parse_milliseconds() → refresh_ms_ (15.6 ms floor) | Pass
exit | Loop ends, thread joined, window restored (exit code 0) | Pass
Only config.txt changes between test cases | marquee-text, refresh-rate, polling-rate read at startup | Pass
Checked by driving the compiled console with injected keystrokes and reading the screen buffer back (Windows 11, 120 × 30).
Notes: Each requirement from the MO3 specification, the code that implements it, and the result of running it. Every command was exercised against the compiled program, including the error paths: invalid set_speed values, empty set_text, unknown and wrong-case commands, a 150-character line, and set_text while the marquee is running.